## Slide 1
Digital Twin-Enabled Intralogistics and Warehouse Control Systems
A Systematic Literature Review
SEN601 Research Techniques and Publication Ethics
Prepared by
Oğuz Kaan Tuğlu
Institution
Hacettepe University
Program
Systems Engineering
Graduate School of Informatics
May 2026 | ogzknttgl@gmail.com
15
primary studies
5
supporting reviews
2021–2026
core publication range
Hacettepe University | Graduate School of Informatics | Systems Engineering
Notes: Slide objective
Open the presentation by clearly introducing the topic, scope, and systematic review perspective.
Speaker note
In this opening slide, I will introduce the title and the academic scope of the study. The presentation focuses on how digital twin technology is used in intralogistics and warehouse control systems. I should emphasize that this is not a general narrative literature review; it is structured as a systematic review-style synthesis based on explicit research questions, search strategy, screening criteria, PRISMA flow, data extraction, and evidence-based interpretation.
The main focus is warehouse and intralogistics control decisions such as order picking, AGV/AMR routing, material handling, internal transport, smart warehouse monitoring, and production-logistics synchronization. Throughout the presentation, I will refer to the included studies using study codes such as S1-S15 for primary studies and R1-R5 for supporting review or contextual studies.
Short summary
This review synthesizes how digital twins are applied to intralogistics and warehouse control, and evaluates the maturity of the available evidence.

## Slide 2
Presentation Overview
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Overview
1
01
Introduction & Background
Why digital twins for warehouse control?
02
Research Questions & PICOS
Structured framework guiding the review
03
Protocol & Search Strategy
Search string, database logic, screening scope
04
Study Selection
PRISMA 2020 flow and eligibility process
05
Study Characteristics
15 primary studies + 5 supporting reviews
06
Quality Assessment
7-criterion appraisal and evidence strength
07
Results — RQ1/RQ2
Application areas and enabling technologies
08
Results — RQ3/RQ4
Performance objectives and research maturity
09
Synthesis & Discussion
Key findings, interpretation, systems view
10
Conclusions
Implications, limitations, and future research
Notes: Slide objective
Give the audience a clear roadmap and show that the presentation follows the expected systematic review structure.
Speaker note
This slide presents the structure of the presentation. I will first explain the research motivation and background problem. Then I will introduce the research questions and the PICOS framework, which define the scope of the review. After that, I will describe the protocol and search strategy, followed by the inclusion and exclusion criteria and PRISMA study selection process.
The middle part of the presentation focuses on the characteristics of included studies, data extraction, and quality or evidence strength assessment. The most important part is the results section, where I answer each research question: application areas, enabling technologies, performance objectives, and research maturity. Finally, I will discuss the key findings, research gaps, limitations, conclusions, and implications for practitioners and future researchers.
Short summary
The presentation follows a systematic review logic: research questions, protocol, study selection, data extraction, quality assessment, results, discussion, and conclusion.

## Slide 3
Introduction & Background
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Introduction
2
The Problem:
Modern warehouses operate as cyber-physical intralogistics systems: material flows, sensors, robots, WMS/WCS data, operators, and control decisions interact continuously.
01
Operational Complexity
Order picking, storage assignment, routing, batching, congestion, and outbound loading interact dynamically.
02
Data-Rich Environment
RFID, IoT sensors, PLCs, AGVs/AMRs, robot telemetry, and WMS logs create continuous operational traces.
03
Need for Evidence
The DT literature is dispersed across logistics, simulation, AI, systems engineering, and Industry 4.0 research.
Objective of this Systematic Review
• Identify where digital twins are applied in intralogistics and warehouse control. • Synthesize enabling technologies, architectures, performance objectives, and maturity levels. • Translate findings into systems engineering implications: lifecycle, V&V, interoperability, human-in-the-loop, and governance.
Background synthesized from the revised systematic review paper and its included study matrix.
Notes: Slide objective
Define the practical problem and explain why digital twins matter in modern warehouse and intralogistics systems.
Speaker note
The main problem is that modern warehouses are no longer simple storage facilities. They are cyber-physical intralogistics systems where physical flows, data flows, human operators, robots, sensors, WMS/WCS software, and operational decisions interact continuously. This makes control decisions more dynamic and more complex than in traditional warehouse environments.
Traditional rule-based or static control approaches may be insufficient when the system includes AGVs, AMRs, conveyors, automated storage, real-time sensor data, and changing order priorities. Digital twins offer a potential solution by creating a dynamic digital representation of the physical warehouse system. This representation can support monitoring, simulation, prediction, optimization, and in more mature cases, adaptive control.
The literature is fragmented across Industry 4.0, simulation, artificial intelligence, warehouse logistics, production logistics, and systems engineering. Therefore, a systematic synthesis is useful to understand what has actually been studied, what evidence exists, and where the research gaps remain.
Short summary
The problem is operational complexity and fragmented evidence; digital twins are a promising decision-support and control capability for warehouse systems.

## Slide 4
Research Questions & PICOS Framework
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
RQ1
Application Areas
What are the main application areas of digital twins in intralogistics and warehouse control systems?
RQ2
Enabling Technologies
Which technologies and architectures are most frequently used in warehouse and intralogistics DT implementations?
RQ3
Performance Objectives
Which operational performance objectives are targeted, such as throughput, picking time, travel distance, congestion, utilization, cost, and energy?
RQ4
Maturity & Gaps
What is the maturity level of current evidence and what research gaps remain for real-time industrial warehouse control?
PICOS Framework
Component
Operationalization in this review
Population / Context
Warehouse, intralogistics, production logistics, order picking, AGV/AMR and material handling systems
Intervention / Technology
Digital twins, digital shadows, CPS models, simulation-based DTs, AI-enhanced DTs, DT-enabled control frameworks
Comparator
Traditional simulation, conventional warehouse control, baseline routing/dispatching rules, or non-DT decision support
Outcomes
Throughput, picking time, travel distance, waiting time, congestion, utilization, cost, energy, resilience
Study Type
Simulation studies, case studies, laboratory prototypes, architecture papers, optimization and implementation studies
The RQs are aligned with the result sections: RQ1/RQ2 address what is used and where; RQ3/RQ4 address impact, maturity, and gaps.
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
RQ & PICOS
3
Notes: Slide objective
Present the research questions and explain how the PICOS framework defines the boundaries of the review.
Speaker note
This slide is the methodological foundation of the review. The research questions guide what I am trying to find in the literature. RQ1 asks which application areas digital twins address in intralogistics and warehouse control. RQ2 asks which enabling technologies and architectures support these applications. RQ3 focuses on the performance objectives and operational outcomes measured in the studies. RQ4 examines the maturity level of the evidence, especially whether studies remain conceptual, simulation-based, prototype-based, case-based, or closer to real industrial implementation.
The PICOS framework helps clarify the scope. The population or context includes warehouses, intralogistics systems, production logistics, order picking, AGV/AMR systems, and material handling systems. The intervention is the use of digital twins, digital shadows, cyber-physical models, simulation-based digital twins, or AI-enhanced digital twin approaches. The outcomes include throughput, travel distance, waiting time, picking time, congestion, utilization, cost, energy, and resilience. The study design includes empirical studies, simulations, prototypes, case studies, and system architecture studies.
Short summary
PICOS makes the review scope defensible and connects the research questions to study selection and data extraction.

## Slide 5
Protocol & Search Strategy
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Protocol & Search
4
Review Protocol
• Pre-defined abstract-level protocol following systematic review logic • Research questions structured using PICOS • All deviations and limitations recorded
Search Scope
• ScienceDirect, SpringerLink, MDPI, Taylor & Francis, IEEE-related and indexed entries • Language: English only • Core range: 2021–2026
Search String Logic
Group A — Digital twin concept:
"digital twin" OR "digital twins" OR "digital shadow" OR "cyber-physical system"
Group B — Intralogistics context:
"warehouse" OR "warehouse logistics" OR "warehouse control" OR "intralogistics" OR "material handling"
Group C — Operational resources:
"order picking" OR "AGV" OR "automated guided vehicle" OR "AMR" OR "autonomous mobile robot"
Combined as: (Group A) AND (Group B OR Group C)
Search strategy reconstructed from Section 4.2 of the revised systematic review.
Notes: Slide objective
Explain the search protocol in a transparent and repeatable way.
Speaker note
This slide explains how the search strategy was constructed. The search logic combines three groups of terms. Group A captures the digital twin concept, including terms such as digital twin, digital twins, digital shadow, and cyber-physical system. Group B captures the warehouse and intralogistics context, including warehouse, warehouse logistics, warehouse control, intralogistics, and material handling. Group C captures operational processes and automated resources, including order picking, AGV, automated guided vehicle, AMR, and autonomous mobile robot.
The combined logic is: Group A AND (Group B OR Group C). This prevents the search from becoming too broad while still capturing relevant warehouse and intralogistics control studies. The main focus is the recent literature, especially the last five years, because digital twin applications in logistics have accelerated with Industry 4.0, AI, IoT, and autonomous mobile robot technologies.
The most important point to say here is that the search strategy was designed to identify studies where digital twins are linked to warehouse or intralogistics decision-making, not merely generic Industry 4.0 discussions.
Short summary
The search strategy combines digital twin terms with warehouse, intralogistics, and operational control terms to form a controlled and relevant corpus.

## Slide 6
Inclusion & Exclusion Criteria
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Study Selection
5
✓ Inclusion Criteria
IC1
Peer-reviewed English-language studies
IC2
Direct relevance to warehouse logistics, intralogistics, material handling, order picking, AGV/AMR coordination, production logistics, or warehouse control
IC3
Explicit DT / digital shadow / CPS concept
IC4
Presents a model, architecture, simulation, prototype, case study, or implementation
IC5
Reports performance, control, decision-support, or operational improvement purpose
✕ Exclusion Criteria
EC1
Generic Industry 4.0 DT papers with no intralogistics relevance
EC2
Macro-level supply chain strategy only
EC3
Non-peer-reviewed webpages, editorials, or commercial material
EC4
DT mentioned superficially with no model, architecture, data link, or control purpose
EC5
Insufficient relevance after abstract screening
Notes: Slide objective
Explain why studies were included or excluded, and show that the study selection process was not arbitrary.
Speaker note
This slide describes the inclusion and exclusion criteria. Studies were included if they were peer-reviewed, written in English, and directly related to warehouse logistics, intralogistics, material handling, order picking, AGV/AMR systems, or warehouse control. They also needed to include a clear digital twin, digital shadow, cyber-physical model, simulation-based DT, or architecture-oriented DT contribution.
Studies were excluded if they were generic Industry 4.0 or supply chain papers without a clear intralogistics or warehouse control focus. Papers were also excluded if they only mentioned digital twins superficially, if they were not academic sources, if they were purely conceptual without sufficient methodological detail, or if they did not provide evidence related to control, performance, or decision support.
A strong sentence to use here is: I did not include every paper that used the phrase digital twin; I included studies that provided evidence relevant to warehouse or intralogistics control.
Short summary
The criteria protect the scope of the review and ensure that included papers directly support the research questions.

## Slide 7
Study Selection
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
PRISMA Flow
6
PRISMA 2020 Flow Diagram →
Identification
Screening
Eligibility
Included
Records identified
through database / search
engine queries
(n = 42)
Records removed before
screening
(n = 7)
Duplicates / non-academic
items removed
Records screened
Title & Abstract
(n = 35)
Records excluded after
abstract screening
(n = 15)
Generic DT / non-logistics /
insufficient relevance
Candidate records
classified by role
(n = 20)
Supporting reviews retained
(n = 5)
R1–R5 used for context
and comparison
Studies included in
qualitative synthesis
(n = 15 primary studies)
S1–S15
PRISMA adapted to abstract-level coursework screening; 15 primary studies + 5 supporting review papers.
Notes: Slide objective
Walk through the PRISMA flow and explain how the final evidence base was obtained.
Speaker note
This slide presents the PRISMA 2020 study selection flow. I will explain it step by step. In the identification stage, records were collected from database searches using the predefined search strings. After removing duplicates and irrelevant non-academic items, the remaining records were screened by title and abstract.
During title and abstract screening, records were excluded if they were generic digital twin papers, non-logistics papers, non-warehouse papers, or insufficiently related to intralogistics control. The remaining papers were then assessed for eligibility based on whether they provided relevant evidence for the research questions. Finally, the corpus was divided into primary studies and supporting review/context papers.
In this review, S1-S15 represent the primary studies used directly in the qualitative synthesis, while R1-R5 represent supporting reviews or contextual studies. I should also be transparent that this is a coursework-level systematic review with abstract-level systematic screening; a publishable full systematic review would require broader database exports, full-text appraisal, and ideally multiple independent reviewers.
Short summary
The PRISMA flow shows how the review moved from the initial search records to the final primary study corpus in a transparent way.

## Slide 8
Characteristics of Included Studies
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Study Characteristics
7
15
Primary studies included
5
Supporting review papers
2021–2026
Core publication range
0
Low relevance after selection
Evidence / Study Type
n
Representative studies
Industrial / case study
5
S1, S3, S8, S14, S15
Simulation / optimization
4
S2, S4, S6, S10
Prototype / laboratory
4
S5, S11, S12, S13
Conceptual / roadmap
2
S9, S10
Supporting review papers
5
R1–R5
Topic Coverage
• Order picking and fulfillment • AGV/AMR routing, capacity and dispatching • Internal transport and material handling • Production–logistics synchronization • Smart warehouse state control and resilience
Included study types and topics from the revised review’s study matrix.
Notes: Slide objective
Characterize the included studies by evidence type and show what kind of corpus the review is based on.
Speaker note
This slide summarizes the general characteristics of the included studies. The final evidence base includes primary studies and supporting review papers. The primary studies are not all of the same type. Some are industrial case studies, some are simulation and optimization studies, some are prototype or laboratory implementations, and some are architecture or roadmap-oriented studies.
This distinction is important because it tells us not only what has been studied, but also how mature the evidence is. For example, simulation-based studies can provide strong analytical insights, but they do not necessarily prove industrial readiness. Prototype studies show feasibility, but not always scalability. Industrial case studies provide stronger practical relevance, but they may be context-specific.
The general finding is that the literature is growing, but the evidence is still concentrated around simulation, prototypes, and limited case studies rather than long-term, closed-loop, real-time industrial deployment.
Short summary
The corpus includes different evidence types, and the overall maturity of the field is promising but still limited.

## Slide 9
Characteristics of Included Studies
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Study Characteristics
8
Source Studies (S1–S15) — 15 primary studies
ID
Study
Primary focus
S1
Kawczynski et al. (2023)
Automated order picking / fulfillment
S2
Legato & Mazza (2026)
Manual order-picking digital shadow
S3
Guerrazzi et al. (2024)
SBS/RS picking–outbound loading balance
S4
Zhang et al. (2024)
AGV dispatching and routing with DRL
S5
Yao et al. (2024)
Smart warehouse DT standardization
S6
Felix-Cigalat & Domingo (2023)
Internal transport optimization
S7
Liu et al. (2024)
Production-logistics synchronization
ID
Study
Primary focus
S8
Zhao et al. (2022)
Spatial-temporal knowledge graph
S9
Li et al. (2022)
Operation twins for synchronization
S10
Ferrari et al. (2022)
Automated warehouse DT roadmap
S11
Vachalek et al. (2021)
CPS testing of logistics algorithms
S12
Rigo et al. (2026)
Material handling DT lab model
S13
Cao & Lei (2022)
DT-driven WMS picking path planning
S14
Hong et al. (2024)
Cross-enterprise synchronization
S15
Zhang et al. (2026)
Opti-state smart warehousing control
Study labels used throughout the deck. Full references provided at the end.
Notes: Slide objective
Introduce the study matrix and directly connect the review findings to specific papers.
Speaker note
This slide is important because it makes the evidence base visible. The study codes S1-S15 identify the primary studies used in the review. For example, S1 by Kawczynski et al. focuses on automated order picking and fulfillment using digital twin concepts. S2 by Legato and Mazza examines manual order picking through digital shadow or digital twin logic. S3 by Guerrazzi et al. focuses on balancing picking and outbound loading in an automated warehouse context.
S4 by Zhang et al. connects digital twin technology with deep reinforcement learning for AGV dispatching and routing. S5 by Yao et al. discusses smart warehouse digital twin standardization. S6 by Felix-Cigalat and Domingo focuses on internal transport optimization. S7 by Liu et al. addresses production-logistics synchronization. S8 by Zhao et al. uses a spatial-temporal knowledge graph for production logistics. S10 by Ferrari et al. proposes a roadmap for automated warehouse digital twins, while S15 by Zhang et al. moves toward opti-state control in smart warehousing.
The key message is that the included papers cover different layers of warehouse control, rather than a single narrow warehouse problem.
Short summary
The study matrix links each result to specific primary studies and makes the evidence traceable.

## Slide 10
Data Extraction
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Data Extraction
9
A standardized extraction form was designed to support cross-study comparison.
Category 1: Bibliographic Information
• Study ID (S1–S15) • Authors and publication year • Publication venue • Primary domain
Category 2: Study Characteristics
• Evidence type • Warehouse / intralogistics context • System boundaries • Maturity level
Category 3: DT Architecture
• Digital twin / shadow type • Data connection and synchronization • Simulation / CPS / AI components • Integration with WMS/WCS/ERP if stated
Category 4: Outcomes
• Performance objective • Evaluation method • Reported improvement direction • Operational relevance
Category 5: Quality Indicators
• Aim clarity • Architecture description • Data connection • Evaluation and metrics • Limitations reported
Handling Missing Data
• If inferable from context → recorded with note • If absent → recorded as “not specified” • No effect-size meta-analysis attempted
Notes: Slide objective
Explain how information was extracted from the studies in a structured way.
Speaker note
This slide explains the data extraction process. For each included study, I extracted bibliographic information, study characteristics, digital twin architecture features, performance outcomes, and quality indicators. Bibliographic information includes the author, year, publication venue, and domain. Study characteristics include evidence type, warehouse or intralogistics context, system boundary, and maturity level.
For the digital twin architecture, I checked whether the study described a digital twin, digital shadow, simulation model, cyber-physical integration, AI component, data synchronization mechanism, or connection to WMS/WCS/ERP systems. For outcomes, I recorded the operational objective, evaluation method, performance metrics, and reported direction of improvement.
If information was clearly inferable from context, it was recorded with a note. If the information was absent, it was marked as not specified. This is important because data extraction makes the comparison across studies more systematic rather than impression-based.
Short summary
The data extraction form supports structured comparison across architecture, method, outcomes, and evidence strength.

## Slide 11
Quality / Evidence Strength Assessment
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Quality Assessment
10
A 7-criterion assessment was applied to each included primary study. Scoring: 0 = not addressed, 1 = partial, 2 = clear; maximum = 14.
Code
Quality Assessment Criterion
QA1
Are objectives / research questions clearly defined?
QA2
Is the digital twin scope clearly described?
QA3
Is the architecture or model described sufficiently?
QA4
Is data connection / synchronization addressed?
QA5
Is the evaluation technique clearly described?
QA6
Are performance metrics reported?
QA7
Are limitations / threats discussed?
11–14
Strong evidence description
7–10
Moderate evidence description
0–6
Weak / insufficient evidence
Preliminary outcome: no included study was excluded solely by quality score; scoring is suggestive due to abstract-level screening.
Quality criteria from Appendix B of the revised review paper.
Notes: Slide objective
Present the quality or evidence strength assessment and explain how evidence maturity was judged.
Speaker note
This slide presents the quality and evidence strength assessment. The scoring rubric uses seven criteria. These include whether the research objectives are clear, whether the digital twin scope is explicitly defined, whether the architecture or model is sufficiently described, whether data connection or synchronization is addressed, whether the evaluation technique is clear, whether performance metrics are reported, and whether limitations or threats are discussed.
Each criterion can be scored from 0 to 2, giving a maximum score of 14. Studies scoring 11 to 14 are considered strong in evidence description, 7 to 10 are moderate, and 0 to 6 are weak. It is important to state that this is an evidence description assessment, not a definitive full methodological risk-of-bias assessment, because the review is based mainly on abstract-level and accessible study information.
The purpose of this scoring is to avoid treating all studies as equally mature. Some papers provide concrete architectures, data sources, and metrics; others remain conceptual or partially described.
Short summary
The quality rubric helps distinguish between strong, moderate, and weak evidence descriptions within the corpus.

## Slide 12
Results — RQ1: Main Application Areas
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
RQ1 Results
11
Application Area
n
Representative studies
Order picking & fulfillment
4
S1, S2, S3, S13
Production–logistics synchronization
4
S7, S8, S9, S14
Internal transport / material handling
3
S6, S11, S12
Smart warehouse control & resilience
3
S5, S10, S15
AGV/AMR dispatching & automated transport
2
S4, S5
Order picking
4
Prod-logistics sync.
4
Transport/material
3
Smart control
3
AGV/AMR
2
Key Finding
The field is concentrated around operational decision points: picking, routing, transport, resource allocation, and synchronization. Digital twins are used mainly to compare scenarios, optimize control rules, and support adaptive planning.
Representative studies: Kawczynski et al. (2023), Legato & Mazza (2026), Guerrazzi et al. (2024), Zhang et al. (2024), Zhao et al. (2022), Hong et al. (2024).
Notes: Slide objective
Answer RQ1 by explaining where digital twins are applied in warehouse and intralogistics control.
Speaker note
This slide answers RQ1. The first major application cluster is order picking and fulfillment. Studies such as S1, S2, S3, and S13 show that digital twins can support picking path planning, fulfillment coordination, scenario testing, and balancing of picking and outbound loading operations.
The second cluster is AGV and AMR dispatching and routing. Studies such as S4, S5, and S12 link digital twins to automated transport resources, route planning, task dispatching, and control of material handling operations. The third cluster is internal transport and material handling, represented by studies such as S6, S11, and S12. The fourth cluster is production-logistics synchronization, where S7, S8, S9, and S14 focus on coordinating material flow between production and logistics processes. The fifth cluster is smart warehouse monitoring and opti-state control, where S10 and S15 are especially relevant.
The overall finding is that digital twins are not restricted to visualization. They are used across several decision layers of warehouse control.
Short summary
Digital twins are most often applied to picking, dispatching/routing, material handling, synchronization, and smart warehouse control.

## Slide 13
Results — RQ2: Enabling Technologies
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
RQ2 Results
12
7+
Simulation / DES base
dominant foundation
6
IoT / RFID / PLC data
physical connection
4
AI / optimization methods
prescriptive control
3
WMS / WCS linkage
integration layer
Technology Group
Representative Studies
Interpretation
Discrete-event / 3D simulation
S1, S2, S3, S5, S10
Core mechanism for scenario comparison and operational experimentation
IoT, RFID, PLC, sensors
S6, S8, S11, S12, S15
Turns static models into synchronized digital shadows / twins
Deep learning, DRL, GA, knowledge graphs
S4, S8, S15
Moves DTs from descriptive monitoring toward adaptive optimization
WMS/WCS/ERP-related structures
S10, S13, S15
Important but often partially specified in current studies
Technology synthesis from S1–S15; review context from Ferrari et al. (2025), Elbouzidi et al. (2023), Aretoulaki et al. (2024).
Notes: Slide objective
Answer RQ2 by connecting enabling technologies to the digital twin applications.
Speaker note
This slide answers RQ2. The most common enabling technology is simulation, especially discrete-event simulation and 3D simulation. Studies such as S1, S2, S3, S6, and S10 use simulation-based approaches to test scenarios, evaluate alternatives, and support warehouse decision-making.
The second technology group is cyber-physical and IoT integration. Sensors, PLCs, robot telemetry, RFID, barcode data, and WMS/WCS logs create the data connection between the physical warehouse and the digital representation. S5, S11, and S12 are important examples here.
The third group is AI and optimization. S4 uses deep reinforcement learning for AGV dispatching and routing. S8 uses a spatial-temporal knowledge graph for state representation. S15 moves toward smart warehouse opti-state control. However, enterprise integration with WMS, WCS, and ERP systems is often underdeveloped. This means the technologies exist, but validated and interoperable architectures are still limited.
Short summary
The main enabling technologies are simulation, IoT/CPS integration, AI/optimization, and enterprise system integration, but integration maturity remains limited.

## Slide 14
Results — RQ3: Performance Objectives
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
RQ3 Results
13
Objective
Studies
Operational meaning
Picking efficiency
S1, S2, S3, S13
Picking time, path length, fulfillment flow, outbound loading balance
Travel / transport reduction
S4, S5, S6
Routing, dispatching, storage distribution, congestion
Resource utilization
S5, S8, S15
AGV capacity, logistics resource allocation, smart warehouse state control
Cost & energy
S4, S6, S15
Reduced movement, optimized schedules, improved state response
Resilience / disturbance response
S7, S14, S15
Production-logistics synchronization under dynamic interference
Interpretation:
Most DTs are evaluated by operational KPIs rather than strategic business metrics; sustainability, human workload, cybersecurity, and lifecycle cost are still underrepresented.
Notes: Slide objective
Answer RQ3 by explaining which performance objectives are measured in the studies.
Speaker note
This slide answers RQ3 by focusing on performance objectives. The most frequently discussed outcomes are operational performance metrics. Picking efficiency appears in studies such as S1, S2, S3, and S13, where the emphasis is on picking time, path length, fulfillment flow, and operational coordination.
Travel distance and internal transport reduction are discussed in S4, S5, and S6 through routing, dispatching, congestion reduction, and storage or resource allocation. Resource utilization appears in S5, S8, and S15, especially in relation to AGV capacity, logistics resource usage, and warehouse state control. Cost and energy appear in studies such as S4, S6, and S15, often as indirect results of shorter movements, better routing, or improved scheduling. Resilience and disturbance response are more visible in production-logistics synchronization studies such as S7, S14, and S15.
A key interpretation is that most papers focus on operational KPIs. Human workload, lifecycle cost, sustainability, cybersecurity, and resilience metrics are still less consistently measured.
Short summary
Digital twin studies mainly measure operational KPIs such as picking time, travel distance, utilization, cost, energy, and synchronization performance.

## Slide 15
Results — RQ4: Research Maturity
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
RQ4 Results
14
5
Case / industrial studies
stronger operational relevance
4
Simulation / optimization
dominant evidence mode
4
Prototype / lab studies
technical feasibility
2
Conceptual / roadmap
early maturity
Maturity Interpretation
• The majority of studies remain simulation-, prototype-, or pilot-oriented. • Only a minority demonstrate continuous bidirectional closed-loop industrial control. • Recent papers move toward AI-enhanced and adaptive control, but V&V, safety assurance, and interoperability are often weakly specified.
Takeaway:
The literature is moving from simulation-based decision support toward real-time, adaptive, and prescriptive warehouse digital twins — but industrial maturity is still limited.
Notes: Slide objective
Answer RQ4 by explaining the maturity level of the research evidence.
Speaker note
This slide answers RQ4. The maturity of the evidence is mixed. Some studies provide industrial or case-study evidence, which is valuable because it is closer to real operational environments. Other studies are simulation or optimization studies, which are useful for exploring alternatives and evaluating decisions under controlled assumptions. Several studies are prototype or laboratory implementations, showing technical feasibility but not necessarily industrial scalability. There are also conceptual or roadmap studies that provide useful direction but limited empirical validation.
The main interpretation is that digital twin research in intralogistics is moving from simulation toward adaptive and AI-enhanced warehouse control, but fully mature industrial deployment is still limited. Very few studies demonstrate long-term, real-time, bidirectional, closed-loop digital twin control in operational warehouses.
From a systems engineering perspective, this matters because a mature digital twin is not just a model. It must be validated, interoperable, maintainable, secure, and useful across the system lifecycle.
Short summary
The field is promising but not fully mature; most studies remain simulation, prototype, or limited case-study based.

## Slide 16
Results — Key Findings per Application Cluster
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
RQ1–RQ4 Findings
15
Order Picking / Fulfillment (S1, S2, S3, S13)
• DTs support scenario testing, picking-path planning, rule comparison, and balancing picking with outbound loading. • Kawczynski et al.; Legato & Mazza; Guerrazzi et al.; Cao & Lei
Transport / AGV / Material Handling (S4, S5, S6, S11, S12)
• DTs combine routing, sensors, PLC/OPC UA, capacity planning, and lab validation for logistics control. • Zhang et al.; Yao et al.; Felix-Cigalat & Domingo; Vachalek et al.; Rigo et al.
Production–Logistics Synchronization (S7, S8, S9, S14)
• DTs coordinate resources across production, intralogistics, and delivery under disturbances. • Liu et al.; Zhao et al.; Li et al.; Hong et al.
Smart Warehouse State Control (S10, S15)
• Research advances toward adaptive opti-state control, synchronized operating environments, and resilience-oriented control. • Ferrari et al.; Zhang et al.
Notes: Slide objective
Synthesize the paper-level findings by application cluster.
Speaker note
This slide brings the results together at the paper level. For the order picking and fulfillment cluster, studies such as Kawczynski et al., Legato and Mazza, Guerrazzi et al., and Cao and Lei show that digital twins can support scenario analysis, path planning, picking coordination, and fulfillment optimization.
For the transport, AGV, and material handling cluster, studies such as Zhang et al., Yao et al., Felix-Cigalat and Domingo, Vachalek et al., and Rigo et al. demonstrate the role of digital twins in routing, dispatching, sensor/PLC integration, capacity planning, and laboratory validation.
For the production-logistics synchronization cluster, Liu et al., Zhao et al., Li et al., and Hong et al. show that digital twins can connect production flow and logistics flow, which is important for system-level coordination. For smart warehouse state control, Ferrari et al. and Zhang et al. indicate that the field is moving toward adaptive control and operational state optimization.
Short summary
The evidence shows that digital twins support multiple intralogistics decision clusters, from picking to smart warehouse state control.

## Slide 17
Discussion — Key Findings & Interpretation
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Discussion
16
01
DTs are mostly decision-support artifacts
The dominant role is comparing scenarios and improving operational choices rather than full autonomous control.
02
Simulation remains the methodological core
DES, 3D simulation, and digital shadows are the strongest foundation for warehouse DT development.
03
AI-enhanced control is emerging
DRL, genetic algorithms, and knowledge graphs indicate a shift toward adaptive and prescriptive DTs.
04
Systems engineering is underdeveloped
Boundaries, stakeholders, interfaces, V&V, lifecycle use, and governance are often weakly explicit.
05
Human-in-the-loop is a major gap
Operators, planners, supervisors, and managers are rarely central in technical DT evaluation.
06
Industrial deployment is still limited
Few studies show robust, long-term, real-time closed-loop integration with WMS/WCS/ERP and physical control systems.
Notes: Slide objective
Interpret the findings rather than simply repeating the results.
Speaker note
This slide is the discussion synthesis. The first key finding is that digital twins are mostly used as decision-support artifacts. They improve visibility, simulation, planning, and optimization, but most are not yet fully autonomous control systems.
The second finding is that simulation remains the methodological core of the field. Many studies use discrete-event simulation, 3D simulation, or digital shadow logic. The third finding is that AI-enhanced control is emerging, especially through deep reinforcement learning, genetic algorithms, and knowledge graphs. The fourth finding is that systems engineering aspects are often underdeveloped. Stakeholder needs, system boundaries, interfaces, validation, traceability, cybersecurity, and lifecycle governance are not always explicitly addressed.
The fifth finding is that human-in-the-loop design is a major gap. Warehouse operators, planners, supervisors, and managers are often mentioned indirectly but not deeply evaluated. The sixth finding is that industrial deployment is still limited. I can summarize the interpretation as: the promise is high, but the maturity is moderate.
Short summary
The literature is technically promising, but it still lacks strong systems engineering treatment, human-centered evaluation, and long-term industrial validation.

## Slide 18
Proposed Systems Engineering-Oriented DT Framework
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Framework
17
Physical layer
layout, racks, conveyors, AGVs/AMRs, workers, docks
Data acquisition
RFID, barcode, IoT sensors, PLCs, WMS logs, robot telemetry
Integration layer
event streaming, APIs, databases, semantic mapping
Modeling layer
DES, 3D simulation, process/resource/spatial models
Analytics & control
forecasting, optimization, routing, dispatching, adaptive rescheduling
Governance & lifecycle
cybersecurity, validation, traceability, requirements, maintenance
SE implication: a mature warehouse DT must be traceable, validated, interoperable, secure, usable, and embedded across lifecycle stages — not only a visualization or simulation model.
Notes: Slide objective
Present the systems engineering-oriented digital twin framework as the synthesis contribution of the review.
Speaker note
This slide presents my synthesized framework. The physical layer includes the actual warehouse elements: layout, racks, conveyors, AGVs, AMRs, workers, docks, and material flows. The data acquisition layer includes RFID, barcode systems, IoT sensors, PLCs, WMS logs, WCS logs, and robot telemetry. These elements provide the real-time or near-real-time data required for the digital twin.
The integration layer connects the physical and digital sides through APIs, event streaming, databases, semantic mapping, or middleware. The modeling layer includes discrete-event simulation, 3D simulation, process models, resource models, and spatial models. The analytics and control layer includes forecasting, optimization, dispatching, routing, adaptive rescheduling, and decision support.
The top layer is governance and lifecycle management. This includes cybersecurity, validation, traceability, requirements, maintenance, and lifecycle updates. The main message is that a mature warehouse digital twin should not be treated as only a visualization or simulation model; it should be treated as a validated and governed system capability.
Short summary
The framework transforms the digital twin from a technical model into a lifecycle-managed systems engineering capability.

## Slide 19
Research Gaps and Future Directions
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Future Research
18
Gap
Current limitation
Future research direction
Real-time synchronization
Many DTs remain simulation-based or digital-shadow-like
Event-driven data pipelines connected to WMS/WCS/robot fleets
Verification & validation
Few studies define V&V protocols against real system behavior
Model accuracy, scenario validity, confidence thresholds
Interoperability
Partial integration with WMS, WCS, ERP, IoT, PLCs
Reference architecture and open interfaces
Human factors
Operators and managers often secondary
Human-in-the-loop trust, usability, training, decision authority
Cybersecurity & governance
DTs increase data dependency and attack surface
Access control, auditability, traceability, privacy-by-design
Sustainability metrics
Energy, emissions and resilience inconsistently measured
Common sustainability/resilience KPIs
Notes: Slide objective
Identify the most important research gaps and future research directions.
Speaker note
This slide presents the research gaps. The first gap is real-time synchronization. Many studies still operate at a simulation or digital-shadow level rather than a fully synchronized digital twin connected to live WMS, WCS, robot fleet, and sensor data. The second gap is verification and validation. Many studies do not clearly explain how accurately the digital twin represents the real warehouse. Future work should define model accuracy, scenario validity, and confidence thresholds.
The third gap is interoperability. Warehouses involve WMS, WCS, ERP, IoT platforms, PLCs, AGVs, and AMRs. More reference architectures and open interfaces are needed. The fourth gap is human factors. Operator trust, usability, decision authority, and human workload are rarely evaluated in depth. The fifth gap is cybersecurity and governance because digital twins increase system connectivity and data dependency. The sixth gap is sustainability and lifecycle metrics, including energy, emissions, resilience, and lifecycle cost.
The message is that the next step should not only be more demos; the field needs reliable, validated, secure, and integrated industrial systems.
Short summary
Future research should focus on real-time integration, V&V, interoperability, human factors, cybersecurity, sustainability, and lifecycle governance.

## Slide 20
Limitations and Threats to Validity
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Limitations
19
AS
Abstract-level screening
The review is coursework-level and based primarily on bibliographic metadata and accessible abstract-level evidence.
DB
Database scope
A fully replicable review should export records from Scopus, Web of Science, IEEE Xplore, ScienceDirect, SpringerLink and ACM DL.
HT
Heterogeneity
Included studies differ in domains, methods, outcomes, validation depth and maturity, limiting direct comparison.
QA
Suggestive quality scoring
Quality assessment may change after detailed full-text appraisal of every study.
SC
Scope boundary
Some included studies address production-logistics synchronization rather than pure warehouse control, but support intralogistics SE insights.
Notes: Slide objective
Report the limitations honestly and show methodological awareness.
Speaker note
This slide presents the limitations and threats to validity. The first limitation is that this review is based on abstract-level systematic screening. Therefore, it is suitable for coursework and qualitative synthesis, but a publishable full systematic review would require full-text screening and more detailed appraisal.
The second limitation is database scope. A stronger review would export records from databases such as Scopus, Web of Science, ScienceDirect, IEEE Xplore, SpringerLink, Taylor & Francis, and ACM Digital Library. The third limitation is heterogeneity. The included studies differ in domain, method, outcome metrics, validation depth, and maturity level, which makes direct comparison and meta-analysis difficult.
The fourth limitation is that the quality scoring is indicative rather than definitive. Full-text appraisal could change the scores. The fifth limitation is scope boundary. Some studies are closer to production-logistics synchronization than pure warehouse control, but they were included because they are relevant to intralogistics systems engineering.
Short summary
The limitations are openly reported to define the interpretation boundary and increase the transparency of the review.

## Slide 21
Conclusions & Implications
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Conclusions
20
Main Conclusion
This review of 15 primary studies indicates that digital twins can improve intralogistics decision quality through simulation-based analysis, resource allocation, routing/dispatching optimization, and adaptive warehouse control. However, most evidence remains simulation-, prototype-, or case-study based rather than mature closed-loop industrial deployment.
For Practitioners & Managers
• Start with high-value operational pain points: picking, routing, congestion, resource utilization. • Treat DT outputs as decision-support until validation and safety assurance are established. • Prioritize interoperability with WMS/WCS/ERP and operator dashboards.
For Future Research
• Longitudinal industrial studies measuring operational and economic impact. • Formal V&V protocols and reference architectures for warehouse DTs. • Human-in-the-loop DT design for trust, usability, and decision authority.
Dissemination & Reporting
Reported using a transparent systematic review structure: RQs, PICOS, search logic, selection criteria, PRISMA flow, data extraction, quality appraisal, synthesis, limitations, and research implications.
Notes: Slide objective
State the main conclusion and separate practical implications from future research implications.
Speaker note
This slide presents the main conclusion. The reviewed primary studies suggest that digital twins can improve decision quality in intralogistics by supporting simulation-based analysis, resource allocation, routing and dispatching optimization, production-logistics synchronization, and smart warehouse control. However, the evidence base is still mainly simulation, prototype, and case-study oriented. Mature, closed-loop, long-term industrial deployment remains limited.
For practitioners, the implication is to start with high-value pain points such as picking efficiency, routing, congestion, resource utilization, and synchronization. Digital twin outputs should initially be used as decision support until the model is sufficiently validated. WMS/WCS/ERP integration and operator-facing dashboards should be prioritized.
For future research, the key needs are longitudinal industrial studies, formal verification and validation protocols, reference architectures, human-in-the-loop digital twin design, cybersecurity analysis, and sustainability metrics.
Short summary
Digital twins offer strong decision-support potential for intralogistics, but industrial maturity requires validation, integration, governance, and human-centered design.

## Slide 22
References — Primary Studies
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
References
21
Primary studies cited in the synthesis (S1–S15)
• S1 Kawczynski et al. (2023). Digital Twin for Complex Logistics Systems: Large-scale automated order picking and fulfillment. • S2 Legato & Mazza (2026). Digital twin solution for manual order-picking operations in a wholesale distribution center. • S3 Guerrazzi et al. (2024). Balancing picking and outbound loading efficiency in an SBS/RS through a digital twin. • S4 Zhang et al. (2024). AGV dispatching and routing integration via digital twin with deep reinforcement learning. • S5 Yao et al. (2024). Simulation-based Digital Twin for smart warehouse: Towards standardization. • S6 Felix-Cigalat & Domingo (2023). Towards a Digital Twin Warehouse through optimization of internal transport. • S7 Liu et al. (2024). DT-based production-logistics synchronization system for satellite mass assembly shop-floor. • S8 Zhao et al. (2022). DT-enabled dynamic spatial-temporal knowledge graph for production logistics resource allocation.
Notes: Slide objective
Show the first part of the reference list and make the evidence base traceable.
Speaker note
This slide lists the first part of the primary studies. I do not need to read every reference in detail during the presentation. Instead, I should explain that the study codes used throughout the results section are expanded here. This makes the synthesis traceable and shows that each claim in the results section is linked to specific studies.
For example, S1, S2, and S3 are mainly used for order picking and fulfillment evidence. S4 is important for AGV dispatching and routing. S5 contributes to smart warehouse digital twin standardization. S6 supports internal transport optimization. S7 and S8 support production-logistics synchronization and knowledge-graph-based state representation.
Short summary
The reference slide supports traceability between the findings and the primary studies.

## Slide 23
References — Primary and Supporting Studies
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
References
22
• S9 Li et al. (2022). Operation twins: production-intralogistics synchronisation in Industry 4.0. • S10 Ferrari et al. (2022). Roadmap towards an automated warehouse digital twin. • S11 Vachalek et al. (2021). Universal cyber-physical model for testing logistics control algorithms. • S12 Rigo et al. (2026). Digital twin of a material handling system based on a physical construction-kit model. • S13 Cao & Lei (2022). Digital Twin-Driven Warehouse Management System for picking path planning. • S14 Hong et al. (2024). DT-based cross-enterprise production-delivery synchronization. • S15 Zhang et al. (2026). Digital twin driven opti-state control approach for smart warehousing. • R1–R5: Ferrari et al. (2025); Elbouzidi et al. (2023); Aretoulaki et al. (2024); Kaiblinger & Woschank (2022); Yao et al. (2023).
Note: Study codes (S1–S15 / R1–R5) are used on result slides to keep academic references visible without overcrowding the presentation.
Notes: Slide objective
Show the remaining primary studies and supporting review/context studies.
Speaker note
This slide shows the remaining primary studies and the supporting review or context studies. S9 addresses operation twins, S10 focuses on a roadmap for automated warehouse digital twins, S11 and S12 relate to cyber-physical testing and material handling, S13 addresses picking path planning, S14 focuses on cross-enterprise production and delivery synchronization, and S15 discusses opti-state control in smart warehousing.
The R-coded sources represent supporting reviews or contextual studies. These were not mixed with the primary evidence in the synthesis, but they helped frame the broader literature on digital twins in intralogistics, AI-based warehouse digital twins, and smart logistics.
A good sentence here is: S1-S15 form the primary evidence base, while R1-R5 support the broader research context.
Short summary
The final reference slide clarifies the distinction between primary evidence and supporting literature.

## Slide 24
Thank You — Questions?
Digital Twin-Enabled Intralogistics and Warehouse Control Systems
Oğuz Kaan Tuğlu
Hacettepe University — Graduate School of Informatics
M.Sc. Systems Engineering
SEN601 Research Techniques and Publication Ethics
ogzknttgl@gmail.com
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
Questions
Notes: Slide objective
Close the presentation professionally and invite questions.
Speaker note
This final slide closes the presentation. I should keep the closing brief and professional. A suitable closing sentence is: Thank you for listening. I would be happy to discuss the methodology, the PRISMA study selection process, the included studies, or the main findings on digital twin-enabled intralogistics and warehouse control systems.
The slide also provides my name, institutional affiliation, program, and contact information. The English institutional title is Hacettepe University - Graduate School of Informatics. The program is M.Sc. Systems Engineering. I should not add a long explanation here; this slide is for transition into the question and answer section.
Short summary
Professional closing slide with author, affiliation, program, and contact information.