## Slide 1
Optimizing Gate Assignments
An Analysis of the Haghani & Chen (1998) Model
Ali Baran Kaya | Oğuz Kaan Tuğlu
Notes: Good morning everyone. Today I'll be presenting an analysis of the 1998 paper by Haghani and Chen titled Optimizing Gate Assignments at Airport Terminals. This work addresses a classic combinatorial optimization problem in airport operations and proposes both a rigorous mathematical formulation and an efficient solution algorithm. My presentation will take approximately ten minutes.

## Slide 2
Why Gate Assignment Matters
Gate shortages during peak operational hours demand highly efficient terminal utilization. Inefficient assignments lead to delays and increased operational costs.
A primary goal for airlines is minimizing passenger walking distances across all types of travelers: transfer, terminating, and originating.
Historically, existing models focused only on single, isolated time periods, failing to account for complex, multi-period overlapping flight schedules that represent real-world operations.
Notes: Let me start by explaining why this problem matters. During peak hours, gate shortages create significant operational costs and passenger frustration. The key insight comes from a 1977 study by Braaksma: at Toronto International Airport's Terminal 2, simply changing the gate assignment policy reduced the average walking distance per passenger from 923 feet in 1973 to 800 feet in 1975 — saving over 100 feet per passenger without any changes to the terminal layout. This demonstrates that smarter assignment policies alone can deliver substantial improvements. The challenge is extending this beyond single time periods to handle real-world overlapping flight schedules.

## Slide 3
QAP Formulation
Successfully formulated a multi-slot Gate Assignment Problem (GAP) as a rigorous Quadratic Assignment Problem (QAP).
Time Dimension
Innovatively incorporated time constraints to effectively handle continuous, overlapping flight schedules across extended periods.
Novel Heuristic
Developed an efficient, highly scalable heuristic algorithm capable of solving large-scale assignment problems in a fraction of standard computing times.
Key Contributions
Notes: The paper makes three distinct contributions. First, it formally models the Gate Assignment Problem as a Quadratic Assignment Problem, or QAP. Second, and this is the key innovation, it incorporates a time dimension to handle multi-slot scheduling — something previous models failed to do. Prior work assumed all aircraft were on the ground simultaneously, which is unrealistic. Third, the authors develop a scalable heuristic algorithm that can handle large real-world instances in practical computation time. These three contributions work together as a coherent whole.

## Slide 4
The core methodology maps the complex Quadratic Assignment Problem to a linear integer program (IP), creating a solvable mathematical framework.
The model assumes a deterministic and static flight schedule, meaning arrival and departure times are treated as fixed planning parameters.
The overarching objective is to minimize total passenger walking distances, carefully distinguishing between the routing needs of transfer passengers and local (originating/terminating) passengers.
Methodology: The Approach
Notes: The methodology operates on two levels. The problem is first formulated as a QAP where the cost of assigning a flight to a gate depends on interactions with all other flight-gate assignments — specifically the passenger transfer volumes and inter-gate distances. Because this quadratic structure is hard to solve directly, the authors linearize it by introducing new binary variables, converting the QAP into an integer linear program. The core decision variable X_ijt equals one if flight i is assigned to gate j during time period t, and zero otherwise.

## Slide 5
Decision Variables
The foundation of the model relies on binary decision variables:
if flight i is assigned to gate j in time period t, 0 otherwise.
To linearize the model, a new variable was introduced:
Objective Function
The goal is to minimize total passenger walking distance across all time periods.
The objective function is expressed as:
Where P represents the passenger transfer volume between flights, and D represents the physical distance between gates.
Mathematical Formulation
Notes: Looking at the mathematical formulation, the objective function minimizes total passenger walking distance for both transfer and local passengers across all time periods. The quadratic product terms X times X prime are replaced by new variables Y_iji'j', which equal one when flight i is at gate j AND flight i-prime is at gate j-prime simultaneously. This substitution is what allows the problem to be solved as a linear integer program using standard branch-and-bound techniques.

## Slide 6
One Gate Per Flight: Every flight must be assigned to one and exactly one gate during its required apron time.
No Overlap: Strict enforcement ensuring no two aircraft may be assigned to the same gate when their physical apron times overlap.
Continuous Dwell: Each aircraft must remain parked at the same assigned gate for the entirety of its scheduled dwell duration.
Mathematical Conservation: Linear constraints ensuring logical consistency between the primary (X) and linearized (Y) decision variables.
Model Constraints & Parameters
Notes: The model enforces four sets of constraints. First, every flight must be assigned to exactly one gate throughout its entire apron time. Second, no two aircraft can share the same gate when their ground times overlap. Third, each aircraft must remain at the same gate for the full duration of its dwell time — it cannot move between gates. Fourth, conservation constraints ensure logical consistency between the X and Y decision variables. Together, these constraints accurately reflect real airport operational requirements.

## Slide 7
1. Initialization
Analyze flight schedules to immediately eliminate decision variables with conflicting gate assignments.
2. Sorting
List all remaining decision variables in increasing order of their passenger walking distance cost.
3. Feasibility
Select the cheapest unlabeled variable. Check if its assignment conflicts with the currently built feasible set.
4. Iteration
Add feasible variables. Repeat until all flights are assigned, generating multiple sets, then select the absolute best.
The Proposed Heuristic Algorithm
Notes: The proposed heuristic operates in four stages. In the initialization step, decision variables corresponding to conflicting flight-gate pairs are eliminated upfront, significantly reducing the search space. Variables are then sorted in ascending order of their cost coefficient — the passenger walking distance. The algorithm greedily selects the cheapest unlabeled variable and checks feasibility against the current partial solution. Multiple feasible solution sets are generated across iterations, and the one with minimum total walking distance is selected. The key advantage is that good solutions are found very early in the search.

## Slide 8
The heuristic approach consistently matched the exact optimal solutions while drastically reducing computational overhead.
Test Case ID | Number of Flights | CPLEX Optimal Solution | Heuristic Best Solution | Execution Time (Heuristic vs CPLEX)
C6481 | 6 | 210,000 | 210,000 | 4.18s vs 871.60s
C7481 | 7 | 41,310 | 41,310 | 8.41s vs 3776.84s
C8492 | 8 | 53,580 | 53,580 | 19.29s vs 12592.60s
C8495 | 8 | 54,720 | 54,720 | 17.36s vs 1616.46s
Results: Heuristic vs. Exact Optimal
Notes: The computational results are striking. For a 6-flight problem, CPLEX finds the optimal solution in 871 seconds while the heuristic finds the identical solution in just 4 seconds — a speedup of over 200 times. For an 8-flight problem the gap widens further: CPLEX takes 12,592 seconds versus only 19 seconds for the heuristic. Critically, both methods reach the exact same objective value in every test case. This means the speed gains come with zero sacrifice in solution quality, which is the key finding for practical applicability.

## Slide 9
Key Insights & Scalability
The proposed heuristic algorithm successfully matches the optimal CPLEX solutions for generated test cases, but accomplishes this in a fraction of the time.
A crucial finding is that the execution time required to find the best solution scales linearly with the number of variables.
This linear scalability proves the algorithm's immense practical value and efficiency for large-scale, real-world airport operations where rapid decision-making is critical.
Notes: The scalability analysis reveals the most important theoretical finding: the time required for the heuristic to find its best solution scales linearly with the number of integer variables. For an NP-hard problem, this is an exceptionally strong result. Furthermore, in virtually all test cases the best solution is found in less than half of the total execution time. This suggests an early stopping rule could be implemented in practice — the algorithm can be terminated well before full convergence and still deliver near-optimal results.

## Slide 10
Real-Time GAP
Extending the model to dynamically re-assign gates in response to unforeseen flight delays and real-time operational disruptions.
Baggage Handling
Incorporating comprehensive baggage transport cost functions, manpower scheduling, and heavy equipment constraints.
Schedule Feedback
Evaluating how insights from gate assignment optimization can inform, critique, and improve initial airline flight scheduling.
Future Research Directions
Notes: The paper identifies three directions for future research. First, extending the model to handle real-time gate reassignment when unforeseen delays disrupt the original plan. Second, incorporating comprehensive baggage transport cost functions together with manpower, vehicle, and equipment constraints for a more realistic total cost model. Third, using gate assignment insights as feedback to evaluate and potentially revise airline flight scheduling decisions. Taken together, these extensions would move toward a fully integrated airport management system.

## Slide 11
Questions?
Thank you for your attention.
Optimizing Gate Assignments at Airport Terminals Haghani & Chen (1998)
Notes: To summarize: Haghani and Chen formulated the multi-slot Gate Assignment Problem as a binary integer QAP with time constraints, and developed a heuristic algorithm that consistently matches optimal solutions while reducing computation time by two to three orders of magnitude. The linear scalability of the algorithm makes it genuinely practical for large airport operations. This paper is a good example of how operations research can bridge rigorous theory and real-world application. I am happy to take any questions.

## Slide 12
https://media.istockphoto.com/id/1477131540/photo/travelers-walking-with-luggage-at-airport.jpg?s=612x612&w=0&k=20&c=yVFByx0UYFu9mmAxuA2ob45phxjch4LO5Ms820JC3s0=
Source: www.istockphoto.com
https://dfjx2uxqg3cgi.cloudfront.net/img/photo/187086/187086_00_2x.jpg?20190906014217
Source: www.youworkforthem.com
https://png.pngtree.com/thumb_back/fw800/background/20250709/pngtree-abstract-representation-of-digital-data-flow-with-vibrant-colors-and-wave-image_17486979.webp
Source: pngtree.com
https://miro.medium.com/v2/resize:fit:1400/1*EXNiT-NvQ8XSSQPS33DldA@2x.jpeg
Source: medium.com
https://fastsolutions.com/wp-content/uploads/2024/12/enclosed-bravo-cart-768x493.png
Source: fastsolutions.com
https://media.hswstatic.com/eyJidWNrZXQiOiJjb250ZW50Lmhzd3N0YXRpYy5jb20iLCJrZXkiOiJnaWZcL2Fpci10cmFmZmljLWNvbnRyb2wtZWxlbWVudHMuZ2lmIiwiZWRpdHMiOnsicmVzaXplIjp7IndpZHRoIjoyOTB9fX0=
Source: science.howstuffworks.com
Image Sources
Notes: Image sources slide — no need to present this during the talk.