## Slide 1
SYSTEMATIC
LITERATURE
REVIEW
Oğuz Kaan Tuğlu
M.Sc. Systems Engineering
Institute of Informatics
Hacettepe University
SEN601 Research Techniques
and Publication Ethics · May 2026
Digital Twin-Enabled
Intralogistics
and Warehouse
Control Systems
15
Primary Studies
5
Supporting Reviews
4
Research Questions

## Slide 2
Presentation Overview
Overview · 1
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
1
01
Introduction & Background
Why digital twins for warehouse control?
02
Research Questions & PICOS
Structured framework guiding the review
03
Protocol & Search Strategy
Search string, database logic, screening scope
04
Study Selection
PRISMA 2020 flow and eligibility process
05
Study Characteristics
15 primary studies + 5 supporting reviews
06
Quality Assessment
7-criterion appraisal and evidence strength
07
Results — RQ1/RQ2
Application areas and enabling technologies
08
Results — RQ3/RQ4
Performance objectives and research maturity
09
Synthesis & Discussion
Key findings, interpretation, systems view
10
Conclusions
Implications, limitations, and future research

## Slide 3
Introduction & Background
Introduction · 2
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
2
The Problem: Modern warehouses operate as cyber-physical intralogistics systems: material flows, sensors, robots, WMS/WCS data, operators, and control decisions interact continuously.
01
Operational Complexity
Order picking, storage assignment, routing, batching, congestion, and outbound loading interact dynamically.
02
Data-Rich Environment
RFID, IoT sensors, PLCs, AGVs/AMRs, robot telemetry, and WMS logs create continuous operational traces.
03
Need for Evidence
The DT literature is dispersed across logistics, simulation, AI, systems engineering, and Industry 4.0 research.
Objective of this Systematic Review
› Identify where digital twins are applied in intralogistics and warehouse control.
› Synthesize enabling technologies, architectures, performance objectives, and maturity levels.
› Translate findings into systems engineering implications: lifecycle, V&V, interoperability, human-in-the-loop, and governance.
Background synthesized from the revised systematic review paper and its included study matrix.

## Slide 4
Research Questions & PICOS Framework
RQ & PICOS · 3
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
3
RQ1
Application Areas
What are the main application areas of digital twins in intralogistics and warehouse control systems?
RQ2
Enabling Technologies
Which technologies and architectures are most frequently used in warehouse and intralogistics DT implementations?
RQ3
Performance Objectives
Which operational performance objectives are targeted, such as throughput, picking time, travel distance, congestion, utilization, cost, and energy?
RQ4
Maturity & Gaps
What is the maturity level of current evidence and what research gaps remain for real-time industrial warehouse control?
PICOS Framework
Component | Operationalization in this review
Population / Context | Warehouse, intralogistics, production logistics, order picking, AGV/AMR and material handling systems
Intervention / Technology | Digital twins, digital shadows, CPS models, simulation-based DTs, AI-enhanced DTs, DT-enabled control frameworks
Comparator | Traditional simulation, conventional warehouse control, baseline routing/dispatching rules, or non-DT decision support
Outcomes | Throughput, picking time, travel distance, waiting time, congestion, utilization, cost, energy, resilience
Study Type | Simulation studies, case studies, laboratory prototypes, architecture papers, optimization and implementation studies
The RQs are aligned with the result sections: RQ1/RQ2 address what is used and where; RQ3/RQ4 address impact, maturity, and gaps.

## Slide 5
Protocol & Search Strategy
Protocol & Search · 4
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
4
Review Protocol
Pre-defined abstract-level protocol following systematic review logic
Research questions structured using PICOS
All deviations and limitations recorded
Search Scope
Scopus (single database) — reproducible, complete, peer-reviewed coverage
Language: English only · Core range: 2021–2026
Search String Logic
Group A — Digital twin concept:
"digital twin" OR "digital shadow"
Group B — Intralogistics context:
"warehouse" OR "intralogistics" OR "material handling" OR "warehouse control" OR "smart warehouse" OR "AS/RS"
Group C — Operational resources:
"order picking" OR "AGV" OR "automated guided vehicle" OR "AMR" OR "autonomous mobile robot"
Combined as: (Group A) AND (Group B OR Group C) | Scopus filters: Article, English, 2021–2026, Digital Twins subject area
Search executed on Scopus. 117 articles retrieved after subject-area filter: "Digital Twins".

## Slide 6
Inclusion & Exclusion Criteria
Study Selection · 5
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
5
✓ Inclusion Criteria
✕ Exclusion Criteria
IC1
Peer-reviewed English-language studies
IC2
Direct relevance to warehouse logistics, intralogistics, material handling, order picking, AGV/AMR coordination, production logistics, or warehouse control
IC3
Explicit DT / digital shadow / CPS concept
IC4
Presents a model, architecture, simulation, prototype, case study, or implementation
IC5
Reports performance, control, decision-support, or operational improvement purpose
EC1
Generic Industry 4.0 DT papers with no intralogistics relevance
EC2
Macro-level supply chain strategy only
EC3
Non-peer-reviewed webpages, editorials, or commercial material
EC4
DT mentioned superficially with no model, architecture, data link, or control purpose
EC5
Insufficient relevance after abstract screening

## Slide 7
Study Selection — PRISMA 2020 Flow
PRISMA Flow · 6
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
6
Identification
Screening
Eligibility
Included
Records identified through
database / search engine queries
n = 117
Records screened
Title & Abstract
n = 97
Candidate records classified by role
n = 40
Studies included in qualitative synthesis
15 primary studies (S1–S15)
Records removed before screening
n = 20
Out-of-scope topics removed (medical, nuclear, construction)
Records excluded after abstract screening
n = 57
EC1–EC5: generic DT, supply chain only, no intralogistics model, superficial DT
Supporting reviews retained
n = 5 (R1–R5)
Used for context and comparison
PRISMA 2020 flow. Scopus single-database search, 117 articles. 15 primary studies (S1–S15) + 5 supporting reviews (R1–R5).

## Slide 8
Characteristics of Included Studies
Study Characteristics · 7
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
7
15
Primary studies included
5
Supporting review papers
2021–2026
Core publication range
0
Low relevance after selection
Evidence / Study Type
Evidence / Study Type | n | Representative Studies
Industrial / case study | 3 | S9, S10, S11
Simulation / optimization | 9 | S1, S2, S4, S5, S6, S7, S8, S14, S15
Prototype / laboratory | 2 | S3, S12
Conceptual / roadmap | 1 | S13
Supporting review papers | 5 | R1–R5
Topic Coverage
Order picking and fulfillment
AGV/AMR routing, capacity and dispatching
Internal transport and material handling
Production–logistics synchronization
Smart warehouse opti-state control and production sync
Included study types and topics from the revised review's study matrix.

## Slide 9
Characteristics of Included Studies
Source Studies (S1–S15) — 15 primary studies
Study Characteristics · 8
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
8
ID | Study | Primary Focus
S1 | Zhang et al. (2024) | AGV dispatching & routing with DRL
S2 | Guerrazzi et al. (2024) | SBS/RS picking–outbound loading balance
S3 | Wu et al. (2024) | DT-based modularized smart warehouse design
S4 | Leng et al. (2021) | DT joint optimisation: packing & storage in AS/RS
S5 | Coelho et al. (2021) | Simulation-based DT for in-house logistics
S6 | Jaoua et al. (2024) | DT+RL framework for AMR dispatching
S7 | Bao et al. (2024) | DT dynamic path planning for multiple AGVs
S8 | Gao et al. (2024) | DT decision support for AGV scheduling
ID | Study | Primary Focus
S9 | Zhang et al. (2026) | DT opti-state control for smart warehousing
S10 | Zhang et al. (2024) | DT multi-granularity sync: production-warehousing
S11 | Su et al. (2025) | DT multi-dim control: production-intralogistics
S12 | Glatt et al. (2021) | DT of material flows via physics simulation
S13 | Pawlewski et al. (2021) | Digital twin lean intralogistics
S14 | Wu et al. (2023) | Dynamic AGV scheduling via digital twin
S15 | Félix-Cigalat & Domingo (2023) | DT warehouse: internal transport optimization
Study labels used throughout the deck. Full references provided at the end.

## Slide 10
Data Extraction
Data Extraction · 9
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
9
A standardized extraction form was designed to support cross-study comparison.
Category 1: Bibliographic Information
Study ID (S1–S15)
Authors and publication year
Publication venue
Primary domain
Category 2: Study Characteristics
Evidence type
Warehouse / intralogistics context
System boundaries
Maturity level
Category 3: DT Architecture
Digital twin / shadow type
Data connection and synchronization
Simulation / CPS / AI components
Integration with WMS/WCS/ERP if stated
Category 4: Outcomes
Performance objective
Evaluation method
Reported improvement direction
Operational relevance
Category 5: Quality Indicators
Aim clarity
Architecture description
Data connection
Evaluation and metrics
Limitations reported
Handling Missing Data
If inferable from context → recorded with note · If absent → recorded as 'not specified' · No effect-size meta-analysis attempted

## Slide 11
Quality / Evidence Strength Assessment
Quality Assessment · 10
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
10
A 7-criterion assessment was applied to each included primary study. Scoring: 0 = not addressed, 1 = partial, 2 = clear; maximum = 14.
Code | Quality Assessment Criterion
QA1 | Are objectives / research questions clearly defined?
QA2 | Is the digital twin scope clearly described?
QA3 | Is the architecture or model described sufficiently?
QA4 | Is data connection / synchronization addressed?
QA5 | Is the evaluation technique clearly described?
QA6 | Are performance metrics reported?
QA7 | Are limitations / threats discussed?
11–14
Strong evidence description
7–10
Moderate evidence description
0–6
Weak / insufficient evidence
Preliminary outcome: no included study was excluded solely by quality score; scoring is suggestive due to abstract-level screening.
Quality criteria from Appendix B of the revised review paper.

## Slide 12
Results — RQ1: Main Application Areas
RQ1 Results · 11
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
11
Application Area | n | Representative Studies
AGV/AMR routing & dispatching | 5 | S1, S6, S7, S8, S14
Internal transport / material handling | 4 | S5, S12, S13, S15
Order picking & storage optimization | 2 | S2, S4
Production-intralogistics sync | 2 | S10, S11
Smart warehouse opti-state control | 2 | S3, S9
Chart: 
| Order picking | Prod-log. sync | Internal transport | Smart WH control | AGV/AMR dispatch
Studies | 2 | 2 | 4 | 2 | 5
Key Finding
AGV/AMR routing dominates (5 studies), followed by internal transport and material handling (4 studies). DTs are applied primarily to closed-loop control, scenario testing, and AI-driven dispatching optimization.
Representative studies: Zhang et al. (2024, JMS), Guerrazzi et al. (2024, FSMJ), Leng et al. (2021, IJCIM), Coelho et al. (2021, CIE), Zhang et al. (2026, RCIM).

## Slide 13
Results — RQ2: Enabling Technologies
RQ2 Results · 12
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
12
9
Simulation / DES base
dominant foundation
6
IoT / RFID / PLC data
physical connection
5
AI / optimization
prescriptive control
3
WMS / WCS linkage
integration layer
Technology Group | Representative Studies | Interpretation
Discrete-event / 3D simulation | S2, S3, S4, S5, S12, S13, S14, S15 | Core mechanism for scenario comparison and operational experimentation
IoT, RFID, PLC, sensors | S5, S9, S10, S11, S12, S15 | Turns static models into synchronized digital shadows / twins
Deep learning, DRL, GA, knowledge graphs | S1, S6, S7, S8, S14 | Moves DTs from descriptive monitoring toward adaptive optimization
WMS/WCS/ERP-related structures | S3, S4, S9 | Important but often partially specified in current studies
Technology synthesis from S1–S15; review context from Aretoulaki et al. (2024, IJCIM, R2) and Ferrari et al. (2024, IJAMT, R3).

## Slide 14
Results — RQ3: Performance Objectives
RQ3 Results · 13
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
13
Order picking & storage
S2, S4
Picking efficiency, outbound loading balance, storage utilization, packing efficiency, throughput
Internal transport / material handling
S5, S12, S13, S15
Resource utilization, material flow accuracy, lean waste reduction, travel distance, cost
AGV/AMR routing & dispatching
S1, S6, S7, S8, S14
Travel time, dispatching efficiency, path length, conflict-free routing, throughput, energy
Smart warehouse opti-state control
S3, S9
Reconfigurability, opti-state maintenance, cost, energy, resilience under disturbances
Production-intralogistics sync
S10, S11
Synchronization accuracy, batch completion time, WIP congestion, disturbance response latency
Interpretation: Most DTs are evaluated by operational KPIs rather than strategic business metrics; sustainability, human workload, cybersecurity, and lifecycle cost are still underrepresented.

## Slide 15
Results — RQ4: Research Maturity
RQ4 Results · 14
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
14
3
Case / industrial studies
stronger operational relevance
9
Simulation / optimization
dominant evidence mode
2
Prototype / lab studies
technical feasibility
1
Conceptual / roadmap
early maturity
Maturity Interpretation
Simulation and optimization studies dominate (9/15), confirming DT-based analysis as the primary mode of evidence. Industrial deployments with closed-loop control are still the minority.
Only 3 studies (S9, S10, S11) demonstrate industrial-scale production-warehousing synchronization with real data integration.
5 studies use DRL/RL (S1, S6, S7, S8, S14), signaling a shift from descriptive to prescriptive DT control; V&V and interoperability remain weakly addressed.
Takeaway: The field is transitioning from simulation-based scenario testing toward real-time adaptive DT control — but industrial-scale closed-loop maturity remains limited.

## Slide 16
Results — Key Findings per Application Cluster
RQ1–RQ4 Findings · 15
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
15
AGV/AMR Routing & Dispatching (S1, S6, S7, S8, S14)
DRL-based DTs outperform rule-based dispatching; physics-accurate simulation enables real-time path planning and conflict-free routing for multi-AGV/AMR systems.
Zhang et al. (2024, JMS); Jaoua et al. (2024, IJCIM); Bao et al. (2024); Gao et al. (2024, EAAI); Wu et al. (2023)
Order Picking & Internal Transport (S2, S4, S5, S12, S13, S15)
Physics-based and DES-driven DTs optimize storage assignment, picking-outbound balance, and internal transport; Lean DT paradigm emerges as a framework for waste elimination.
Guerrazzi et al. (2024); Leng et al. (2021, IJCIM); Coelho et al. (2021, CIE); Glatt et al. (2021, JMS); Félix-Cigalat & Domingo (2023)
Production-Intralogistics Synchronization (S10, S11)
Multi-granularity and multi-dimensional DT control frameworks reduce batch WIP congestion and improve production-warehousing coordination under dynamic disturbances.
Zhang et al. (2024, IJPR); Su et al. (2025, JMS)
Smart Warehouse Opti-State Control (S3, S9)
Modular DT design (Wu et al.) enables rapid warehouse reconfiguration; Zhang et al. (RCIM) demonstrates opti-state DT sustaining performance under real-time dynamic disturbances.
Wu et al. (2024, IJCIM); Zhang et al. (2026, RCIM)

## Slide 17
Discussion — Key Findings & Interpretation
Discussion · 16
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
16
01
DTs are shifting from decision-support to prescriptive control
Early studies (Coelho, Pawlewski) used DTs for logistics decision support; recent work (Zhang 2026 RCIM, Su 2025) demonstrates real-time adaptive closed-loop control.
02
Simulation and DRL are the dual methodological pillars
DES and physics simulation (9 studies) remain the dominant DT foundation; 5 studies integrate DRL (S1, S6, S7, S8, S14), marking a clear methodological shift.
03
AI-enhanced adaptive control is the leading trend
DRL-based DTs (Zhang 2024 JMS, Jaoua 2024, Bao 2024, Gao 2024) outperform rule-based dispatching in AGV/AMR routing — the fieldâs strongest evidence cluster.
04
V&V and interoperability remain major gaps
No study provides formal V&V protocols or reference architectures; WMS/WCS integration is partial in most implementations (S3, S4, S9 as exceptions).
05
Human-in-the-loop and sustainability are major gaps
Only Drissi Elbouzidi et al. (2025, R5) addresses sustainability; no primary study centers the human operator in DT evaluation design.
06
Industrial-scale closed-loop deployment is still rare
Only S9, S10, S11 demonstrate industrial synchronization with real data; most evidence remains simulation-based, limiting generalizability.

## Slide 18
Proposed Systems Engineering-Oriented DT Framework
Framework · 17
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
17
Physical layer
layout, racks, conveyors, AGVs/AMRs, workers, docks
Data acquisition
RFID, barcode, IoT sensors, PLCs, WMS logs, robot telemetry
Integration layer
event streaming, APIs, databases, semantic mapping
Modeling layer
DES, 3D simulation, process/resource/spatial models
Analytics & control
forecasting, optimization, routing, dispatching, adaptive rescheduling
Governance & lifecycle
cybersecurity, validation, traceability, requirements, maintenance
SE implication: a mature warehouse DT must be traceable, validated, interoperable, secure, usable, and embedded across lifecycle stages — not only a visualization or simulation model.

## Slide 19
Research Gaps and Future Directions
Future Research · 18
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
18
Gap | Current Limitation | Future Research Direction
Real-time synchronization | 9/15 studies are simulation-based; only 3 show industrial real-time data integration | Event-driven pipelines connecting WMS/WCS to physics-accurate simulation models
Verification & validation | No primary study defines formal V&V; Ferrari et al. (R3) proposes AS/RS model validation | Model accuracy, scenario validity, confidence thresholds
Interoperability | WMS coupling present in S3, S4, S9 only; no full WCS/ERP integration demonstrated | Open DT reference architecture with standardized WMS/WCS interfaces
Human factors | No primary study evaluates human-in-the-loop or operator trust in DT-driven decisions | Human-centered DT evaluation: usability, trust calibration, and decision authority
Cybersecurity & governance | Increased IoT and data integration raises cybersecurity and privacy risks; not addressed in corpus | Access control, auditability, traceability, privacy-by-design
Sustainability metrics | Only Drissi Elbouzidi et al. (R5) addresses carbon accounting; S9 includes energy as KPI | Standardized energy, emission, and resilience KPIs across warehouse DT implementations

## Slide 20
Limitations and Threats to Validity
Limitations · 19
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
19
AS
Abstract-level screening
The review is coursework-level and based primarily on bibliographic metadata and accessible abstract-level evidence.
DB
Database scope
This review used Scopus as the single database (117 articles). Multi-database replication (WoS, IEEE Xplore, ACM DL) would improve completeness.
HT
Heterogeneity
Included studies differ in domains, methods, outcomes, validation depth and maturity, limiting direct comparison.
QA
Suggestive quality scoring
Quality assessment may change after detailed full-text appraisal of every study.
SC
Scope boundary
Some included studies address production-logistics synchronization rather than pure warehouse control, but support intralogistics SE insights.

## Slide 21
Conclusions & Implications
Conclusions · 20
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
20
Main Conclusion
This Scopus-based review of 15 primary studies confirms that DTs improve intralogistics through simulation-driven scenario testing (9 studies), AI-enhanced AGV/AMR dispatching (5 DRL studies), and production-warehousing synchronization (3 industrial studies). Evidence quality is predominantly moderate-to-strong, but industrial closed-loop deployment at scale remains rare.
For Practitioners & Managers
For Future Research
› Longitudinal industrial studies with production-connected DTs measuring operational and economic impact.
› Formal V&V protocols and open reference architectures enabling WMS/WCS/AGV DT interoperability.
› Human-in-the-loop DT design for trust, usability, and decision authority.
Dissemination & Reporting
Reported using a transparent systematic review structure: RQs, PICOS, search logic, selection criteria, PRISMA flow, data extraction, quality appraisal, synthesis, limitations, and research implications.

## Slide 22
References — Primary Studies
References · 21
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
21
Primary studies cited in the synthesis (S1–S15)
S1
Zhang et al. (2024). AGV dispatching and routing integration via DT with deep reinforcement learning. Journal of Manufacturing Systems. DOI: 10.1016/j.jmsy.2023.12.008
S2
Guerrazzi et al. (2024). Balancing picking and outbound loading efficiency in an SBS/RS through a digital twin. Flexible Services & Manufacturing Journal. DOI: 10.1007/s10696-024-09554-w
S3
Wu et al. (2024). A digital twin-based modularized design approach for smart warehouses. Int. J. Computer Integrated Manufacturing. DOI: 10.1080/0951192X.2023.2278100
S4
Leng et al. (2021). Digital twin-driven joint optimisation of packing and storage assignment in large-scale AS/RS. IJCIM. DOI: 10.1080/0951192X.2019.1667032
S5
Coelho et al. (2021). Simulation-based decision support tool for in-house logistics: the basis for a DT. Computers & Industrial Engineering. DOI: 10.1016/j.cie.2020.107094
S6
Jaoua et al. (2024). DT-based reinforcement learning framework: application to AMR dispatching. IJCIM. DOI: 10.1080/0951192X.2024.2314787
S7
Bao et al. (2024). A DT-driven dynamic path planning approach for multiple AGVs. Proc. IMechE Part B. DOI: 10.1177/09544054231180513
S8
Gao et al. (2024). A digital twin-based decision support approach for AGV scheduling. Engineering Applications of AI. DOI: 10.1016/j.engappai.2023.107687

## Slide 23
References — Primary and Supporting Studies
References · 22
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601
22
S9
Zhang et al. (2026). DT driven opti-state control for smart warehousing. Robotics & Computer-Integrated Manufacturing. DOI: 10.1016/j.rcim.2025.103099
S10
Zhang et al. (2024). DT multi-granularity synchronisation for production-warehousing. Int. J. Production Research. DOI: 10.1080/00207543.2024.2408671
S11
Su et al. (2025). DT multi-dimensional control for dualistic production-intralogistics synchronisation. JMS. DOI: 10.1016/j.jmsy.2025.07.020
S12
Glatt et al. (2021). Modeling and implementation of a DT of material flows via physics simulation. JMS. DOI: 10.1016/j.jmsy.2020.04.015
S13
Pawlewski et al. (2021). Digital twin lean intralogistics: research implications. Applied Sciences. DOI: 10.3390/app11041495
S14
Wu et al. (2023). Dynamic scheduling and optimization of AGV in factory logistics via DT. Applied Sciences. DOI: 10.3390/app13031762
S15
Félix-Cigalat & Domingo (2023). Towards a DT warehouse through optimization of internal transport. Applied Sciences. DOI: 10.3390/app13084652
R1–R5
R1: Stączek et al. (2021) Sensors | R2: Aretoulaki et al. (2024) IJCIM | R3: Ferrari et al. (2024) IJAMT | R4: Lee et al. (2026) IJPR | R5: Drissi Elbouzidi et al. (2025) Cleaner Logistics & Supply Chain
Note: Study codes (S1–S15 / R1–R5) are used on result slides to keep academic references visible without overcrowding the presentation.

## Slide 24
Thank You
Questions and discussion are welcome.
Digital Twin-Enabled Intralogistics and Warehouse Control Systems:
A Systematic Literature Review
Oğuz Kaan Tuğlu
M.Sc. Systems Engineering
Institute of Informatics
Hacettepe University
SEN601 Research Techniques
and Publication Ethics · May 2026
ogzknttgl@gmail.com
Digital Twin-Enabled Intralogistics — Systematic Review | SEN601